## Slide 1: Adaptive Air Pressure Regulation System

## Slide 2: Problem Statement
What problem are we solving?
Sudden external pressure variations can cause:
  Ear discomfort
  Fatigue
  Reduced situational awareness
Passive ear muffs cannot adapt to dynamic pressure changes
Key Challenge:
  Maintain a safe and comfortable pressure difference between the ear cavity and the external environment.

## Slide 3: Problem Statement

## Slide 4: Proposed Solution (System Overview)
Solution Overview:
Two pressure sensors:
  Inside Ear Muff Sensor
  Outside Ear Muff Sensor
A solenoid valve to regulate air pressure
Intelligent control logic with timing control
Data logging + Web-based monitoring
High-level idea:
  Continuously monitor pressure difference and regulate airflow using a solenoid valve.

## Slide 5: Hardware Components
Main Components:
ESP32 Microcontroller
2 × DPS310 Pressure Sensors
Solenoid Valve (Air Vent)
MOSFET / Driver Circuit
Power Supply
Ear Muff Enclosure
Why DPS310?
High-resolution pressure sensing
Suitable for small differential pressure measurement

## Slide 6: Sensor Placement Strategy
Sensor Placement:
Sensor 1 (Inside): Measures ear cavity pressure
Sensor 2 (Outside): Measures ambient pressure
Reason:
Enables differential pressure calculation
Eliminates false triggering due to absolute pressure drift

## Slide 7: Differential Pressure Principle (Formulas)
Differential Pressure Calculation:
Where:
= External pressure
= Pressure inside ear muff
Trigger Condition:
If the threshold is crossed → Valve Actuation Starts

## Slide 8: Solenoid Valve Control Logic
Valve Actuation Pattern:
ON → 500 ms
OFF → 500 ms
ON → 500 ms
OFF → 500 ms
Then rest period: 5–15 seconds (user-defined)
Purpose:
Gradual pressure equalization
Prevents sudden air bursts
Reduces mechanical wear

## Slide 9: Timing Diagram (Formula-Based Explanation)
Total Active Time:
Total Cycle Time:
Where:
seconds (user configurable)

## Slide 10: Firmware Architecture
Software Modules:
Sensor Interface (I²C)
Baseline Calibration
Differential Pressure Logic
Valve FSM (Finite State Machine)
SPIFFS File System
Async Web Server

## Slide 11: Valve Finite State Machine (FSM)
FSM States:
IDLE
VALVE_ON
VALVE_OFF
WAIT
State Transition Logic:
Based on:
  Time elapsed
  Pressure difference
  User-defined delay

## Slide 12: Data Logging using SPIFFS
Why SPIFFS?
Lightweight flash-based file system
No external storage required
Stored Data (CSV):
  Timestamp, P_inside, P_outside, Delta_P, Delay_Time, Feedback
Advantages:
Post-analysis
Debugging
Performance evaluation

## Slide 13: Data Logging using SPIFFS

## Slide 14: Web Server & Dashboard
ESP32 Web Server Features:
Real-time pressure display
Valve status
User configuration:
  Threshold
  Wait time
Technologies Used:
Async Web Server
HTML, CSS, JavaScript

## Slide 15: Web Server & Dashboard

## Slide 16: Applications
Potential Use Cases:
Industrial safety ear protection
Pilots & aviation ground crew
Construction sites
Research labs

## Slide 17: Conclusion & Future Scope
Conclusion:
Intelligent ear protection system
Combines sensing, actuation, and web monitoring
Adaptive & configurable
Future Enhancements:
Closed-loop PID control
Mobile app integration
Miniaturization
ML-based pressure prediction